## Slide 1: Weekly water availability prediction
October 2026
Yang Chen, Sean Turner, Haoran Niu, Dali Wang

## Slide 2
Data Inputs and prediction target
Predictor | Source and processing | Model unit
Precipitation | Daymet daily precipitation, summed over 7 days | mm/week
Temperature | Daymet daily (Tmax + Tmin)/2, averaged over 7 days | °C
Runoff | NLDAS-2 Noah surface runoff + baseflow, summed | mm/week
Elevation | Area-weighted mean of the supplied elevation grid | m, static
Prediction target: Estimated Local Flow (ELF) is the reference target. Totally 52 locations (30 reservoirs + 22 river gauges)
ELF is not automatically total downstream inflow. Nickajack remains a model node but has no valid test reference.

## Slide 3
Shared LSTM + GNN + site-specific heads
13 weekly steps
P, T, runoff, elevation
Shared LSTM
64 learned features
3 GNN layers
Upstream feature exchange
Site-specific head
One ELF estimate
LSTM learns time patterns
The same weights process each site’s own history, including the target week.
GNN adds upstream context
52 nodes and 49 directed links. Three layers reach at most three upstream links.
Each site has its own head
A small 64-to-1 mapping with Softplus produces a nonnegative estimate.
46,068 trainable parameters

## Slide 4
Training, validation, testing
Role | Target period | Eligible site-weeks
Training | 1982–2004 | 50,084
Validation | 2005–2009 | 9,868
Testing | 2010-01-04 to 2016-10-09 | 15,025

## Slide 5
weekly NSE at each location
The median NSE for all locations is 0.826.
Chilhowee remains below zero.
Nickajack is not scored because no valid test reference remains.

## Slide 6
Separate XGBoost models
A simpler per-site benchmark uses the same weekly inputs, data splits
52 independent regressors
Chart: Mean share of training split gain
| Elevation | Temperature | Precipitation | Runoff
Mean share of training split gain | 0 | 0.03659 | 0.23227 | 0.73114
Runoff dominates tree split gain. This is descriptive importance, it describes how the fitted trees used in the inputs. It does not measure causal value or the effect of removing runoff.
Mean NSE of all location: 0.773

## Slide 7
XGBoost minus site-head NSE
Positive values favor XGBoost. Negative values favor the shared LSTM + GNN + site-head model.
Chart: NSE difference
| ELF26 Whitwell | ELF25 South Chickamauga Creek | ELF24 Charleston | ELF23 Ocoee No. 1 | ELF22 Copperhill | ELF21 Blue Ridge | ELF20 Apalachia | ELF19 Hiwassee | ELF18 Nottely | ELF17 Chatuge | ELF16 Oakdale | ELF15 Melton Hill | ELF14 Clinton | ELF13 Norris | ELF12 Tellico | ELF11 Chilhowee | ELF10 Fontana | ELF09 Maryville | ELF08 Cherokee | ELF07 Kingsport | ELF06 Boone | ELF05 Elizabethton | ELF04 Watauga | ELF03 South Holston | ELF02 Sevierville | ELF01 Douglas
NSE difference | -0.053636 | -0.068074 | -0.13698 | 0.0097238 | -0.028818 | -0.033086 | -0.039378 | -0.00068327 | -0.0077912 | -0.03523 | -0.021249 | -0.0492 | -0.040692 | -0.056482 | -0.034597 | 0.1312 | -0.024614 | -0.058554 | -0.011499 | -0.10523 | -0.016551 | 0.026858 | -0.10893 | -0.02792 | -0.046819 | -0.022838
Chart: NSE difference
| ELF52 Savannah | ELF51 Pickwick | ELF50 Wilson | ELF49 Wheeler | ELF48 Decatur | ELF47 Guntersville | ELF45 Chickamauga | ELF44 Watts Bar | ELF43 Fort Loudoun | ELF42 Knoxville | ELF41 Hurricane Mills | ELF40 Shelbyville | ELF39 Normandy | ELF38 Lobelville | ELF37 Bishop | ELF36 Cedar Creek | ELF35 Little Bear Creek | ELF34 Bear Creek | ELF33 Upper Bear Creek | ELF32 Iron City | ELF31 Prospect | ELF30 Fayetteville | ELF29 Tims Ford | ELF28 Chase | ELF27 Woodville
NSE difference | -0.23966 | -0.053489 | -0.1129 | -0.081467 | -0.028686 | -0.047991 | -0.035375 | -0.013111 | -0.1062 | -0.10196 | 0.042151 | -0.091025 | -0.059964 | 0.030398 | -0.066239 | -0.065816 | -0.035546 | -0.15287 | -0.0011129 | -0.019353 | -0.050059 | -0.069648 | -0.025124 | -0.066227 | -0.034265

## Slide 8
Regional CAMELS pretraining
47 regional watersheds provide additional training examples before TVA fine-tuning.
Pretrain the shared LSTM
Weekly P, T, runoff and elevation
USGS streamflow targets, not TVA ELF
Fine-tune on unchanged TVA data
Transfer only LSTM weights.
Initialize GNN and site heads anew.
Train all components on the TVA training split.
Median NSE 0.824 vs 0.826
17 sites improve, 34 worsen.

## Slide 9
CAMELS comparison and interpretation
Regional pretraining does not improve median NSE in this single experiment.
Possible explanations include target mismatch and domain differences. These hypotheses were not isolated by the experiment.